Treatability of Tannery Waste Water in Kano City of Nigeria.

Solomon, B.O1*; Yusuf, R.O.2; Onyia, O.C1; Abdullahi M.S1   and Adetunji, O.A1

1National Biotechnology Development Agency,

No.16 Dunukofia Street, Former C.A.C. Building, Area 11,

P.M.B. 5118, Wuse, Abuja, Nigeria.

2 University of Ilorin,

P.M.B. 1515, Ilorin, Kwara State, Nigeria.

ABSTRACT

Tanneries have gained negative image in the society because of the high polluting nature of their effluents. A typical tanning company consumes as much as 400 kg sodium sulphide; 250 kg ammonium sulphate; 820 kg sodium chloride; 80 kg sulphuric acid; 740 and 40 kg of lime and sodium carbonate per production day and with about 32 of such companies in Kano, the tanning process is simply the most environmentally polluting industry because of the enormous discharge into the water bodies such as the Challawa and Jakara rivers. Effluent from the tanneries is 225 m3/day and 12 tons of solid waste per day amounting to gross pollution of the environment all year round. The effluent from tannery industries in Kano were collected and characterized in the course of this study. Because of the expensive nature of conventional treatment, biological methods were considered for the treatability of the waste through the use of microorganisms. Hence, the bioremediative potentials of microorganisms isolated from tannery wastewater were evaluated. Seven microorganisms were isolated and were also characterized biochemically. These were used on a sample of supplemented tannery wastewater to determine biomass growth, specific growth rate and their effectiveness in relation to pH, chemical oxygen demand (COD), total suspended solids (TSS) and chloride. The microorganism shows capability for bioremediation of the tanneries waste hence could be effective for the overall management of tannery wastewater in Kano City.

Key Words: Tannery industries, Bioremediation, Waste water, Microorganism and Environment

*Corresponding author: bosconsult@yahoo.com , 08034049111, 08051277953

1.0	INTRODUCTION

Tanning is the key operation that transforms raw skins into leather. It is the act of converting animal hides and skins into leather. These are made principally of proteins and also contain minor amounts of lipids, albumins, globulin, and carbohydrates (World Bank, 1998). Only 20–25% of the raw hide weight is processed to leather (UNIDO, 2000; UNEP/IEO (1994)). Tanning also involves a complex combination of mechanical and chemical processes. The heart of the process is the tanning operation itself in which organic or inorganic materials become chemically bound to the protein structure of the hide and preserve it from deterioration. The preliminary tannery processes or beam house processes (cleaning, trimming, deliming, etc.) prepare the hide protein so that all the undesirable impurities are removed, leaving the skin in a receptive condition to absorb the chromium, vegetable, or occasionally other tanning agents used in subsequent tanning operations. Nigeria's leather industry plays an important role both as an earner of foreign exchange and provider of employment. Tanning and finishing of leather in the mechanized way started in Kano, Nigeria in 1949 (Buba et al., 2004). A typical tanning company consumes as much as 400 kg sodium sulphide; 250 kg ammonium sulphate; 820 kg sodium chloride; 80 kg sulphuric acid; 740 and 40 kg of lime and sodium carbonate per production day and with about 32 of such companies in Kano, the tanning process is simply the most environmentally polluting industry because of the enormous discharge into the water bodies such as the Challawa and Jakara rivers. Liquid waste water from the tannery is 225 m3/day and 12 tons of solid waste per day amounting to gross pollution of the environment year round. The economic benefits derived from the leather industries are enormous. However, the negative environmental impact of their wastewater is a major setback (Rao et al., 1999). Most of the tanneries in Nigeria use old and inefficient technologies and production methods contrary to the concept of cleaner technology. The use of inefficient technology is largely responsible for the wasteful use of water and chemicals, high load of effluent pollutants and low productivity of the tanning industry (MAPS, 2002). The harmful effects of effluents and waste products from different industries have been reported by  Tripathi (1978), Chin et al., (1987), Chadderton (1988), Ramasami et al., (1999), Rao et al., (1999), Naidu (2000), Kamaludeen et al., (2003), Cuenza, (2004), Yusuf (2004), and Yadav et al., (2005). Because of the expensive nature of conventional treatment, biological methods were sought through the use of microorganisms. Hence, this study was to evaluate the bioremediative potentials of microorganisms isolated from tannery wastewater.

2.0	MATERIAL AND METHODS

2.1	Characterization of the wastewater

Tannery wastewater was taken at ambient conditions from the storage pond of the Tanning Industries and analysed in accordance with HACH, 1997; APHA, 1998. The wastewater was later characterised in the Microbiology Laboratory, Obafemi Awolowo University, Ile-Ife, Osun State, Nigeria to determine the following polluting parameters, Alkalinity, Total solids (TS), Total dissolved solids (TDS), Total suspended solids (TSS), Biochemical oxygen demand (BOD), Chemical oxygen demand (COD), Chromium and Chloride.

2.2	Isolation & Characterisation of the microorganisms from the wastewater

The micro organisms in the wastewater were isolated in the Microbiology Laboratory, Obafemi Awolowo University, Ile-Ife, Osun State, Nigeria using standard methods. The characterization was carried out according to Seely and Demark, 1972; Hughes and Leffson, 1953; Holding and Collee 1971; Harrigan and MacCance, 1966.

  - Nutrient preparation for primary and secondary cultures

The nutrient preparation for Primary and Secondary Cultures was prepared using the following Salts: KH2PO4 1.6mg/l, NaHPO4.2H2O 3.1mg/l, NH4NO3  0.5mg/l, KNO3 2.0mg/l, MgSO4.7H2O 0.1mg/l, CaCl2.2H2O 0.02mg/l, Boric acid 0.1mg/l, ZnSO4.7H2O 0.04mg/l, Mo salt 0.02mg/l, MnSO4 0.04mg/l, CuSO4 0.04mg/l, FeSO4.7H2O 0.0025mg/l (Leahy and Colwell, 1990; Atlas and Bartha, 1992; Prince, 1992; Pritchard et al., 1992; Leavitt and Brown, 1994).

2.4	Experimentation

Two hundred millilitre of fresh medium from the secondary culture was added to each flask (250ml) and 1% v/v of the wastewater was added. Using an inoculating loop that had been sterilised to redness in a flame and cooled by oscillating briefly in the air, three loops of microorganism were streaked into each labelled flask. The flasks were then placed on the gyratory incubator shaker at 30oC and 120rpm for 84 hours. Samples were withdrawn every six hours for the analysis of pH, chloride, total suspended solid and COD. These four parameters were part of the parameters determined for the fresh sample of wastewater at the time of sample collection. They are part of the Group I parameters, i.e. the most significant parameters for which effluent threshold will most often be set (FEPA, 1991). The other parameters like colour, odour, temperature and chloride are among those in Group II, (i.e. additional parameters).

3.0	ANALYTICAL METHOD

The samples was analysed using HACH spectrophotometer DR 2010 and the reference standard was according to APHA, (1998) and FEPA, (1991)

4.0	RESULTS AND DISCUSSION

Table 1.0 shows the result of the tannery effluent sample analysis for certain pollution parameters and the national effluent limit for each parameter was also included for comparison. The result showed that the pollution levels for some of the measured parameters in the effluent were very high with the exception of temperature and pH. The pattern of the characterization showed similar trends with earlier works (Tünay et al., 1995; Orhon et al., 1999; Rivela et al., 2002; More et al., 2002; Tare et al., 2003; Yadav et al., 2005). Only seven microorganisms with bioremediation potentials were isolated and identified as Micrococcus sp.; Staphylococcus aureus; Bacillus subtilis; Proteus vulgaricus; Pseudomonas fragii; Pediococcus halophilus and Staphylococcus aureus;

Table 1.0: Tannery effluent analysis

| Parameter | Measurement A | Measurement B | Average | *National limit |
| --- | --- | --- | --- | --- |
| Temperature (oC) | 29 | 24 | 26.5 | 40 |
| Alkalinity | 8.76 | 9.78 | 9.27 | - |
| Total solids | 3520 | 3670 | 3595 | 2040 |
| Total dissolved solids | 2718 | 2720 | 2719 | 2000 |
| Total suspended solids | 872 | 880 | 876 | 40 |
| Sulphide | 170 | 175 | 172.5 | 1 |
| BOD5 | 2163 | 2117 | 2140 | 100 |
| COD | 4373 | 4397 | 4385 | 160 |
| Chromium | 42.3 | 42.7 | 42.5 | 2.0 |
| Chloride | 129.12 | 125.04 | 127.08 | 50 |

* (FEPA, 1991)

All values are in mg/l unless otherwise stated.

The biomass growths of the individual microorganisms were initially very slow until after forty hours (Fig. 1). This was the lag phase where the microorganisms were adjusting and acclimatising to their environment. The biomass growths picked up rapidly (log phase) and continued till when the nutrients were exhausted or probably when the metabolic products they formed inhibited further multiplication. This was after seventy–two (72) hours when stagnation set in. The microorganism with the highest growth was Pediococcus halophilus (3.01g/l). The growth level for the other microorganisms are Proteus vulgaricus (2.55g/l), Pseudomonas fragii (2.34g/l), Streptococcus faecium (1.66g/l), Bacillus subtilis (0.96g/l), Micrococcus sp. (0.61g/l) and Staphylococcus aureus (0.60g/l). The growth patterns for individual microorganisms followed the well-accepted pattern of microbial growth kinetics (Ramos and Timis, 1987; Horner, 1993; Lee and Lin, 1999). Although they were in varying degrees, the patterns could be identified as the lag, acceleration, exponential or log, deceleration, and stationary phases (Lee and Lin, 1999).The microorganism with the individual highest specific growth rate of 0.01494 hr–1 was Proteus vulgaricus. The specific growth rate (Fig. 2) for the other microorganisms were 0.01448 hr–1 for Pseudomonas fragii, 0.01378 hr–1 for Pediococcus halophilus, 0.01348 hr–1 for Micrococcus sp., 0.01320 hr–1 for Streptococcus faecium, 0.01295 hr–1 for Staphylococcus aureus and 0.01277 hr–1 for Bacillus subtilis. Fig. 3 showed the variation of chemical oxygen demand (COD) with time for all the seven microorganisms. The positive aspect was that there was a significant reduction in the COD value and this will reduce the pollution load of the receiving water body. The microorganisms displayed very high abilities in bringing down the concentration of total suspended solids (TSS) as shown in Fig. 4. The best microorganism, Bacillus subtilis, exhibited the greatest potential after fifty–two hours. The result showed that five of the microorganisms could be used for the reduction of total suspended solids. These are Bacillus subtilis, Pseudomonas fragii, Proteus vulgaricus, Micrcoccus sp. and Pediococcus halophilus. Only Pseudomonas fragii was able to bring the chloride concentration to 57.72mg/l, which is close to the national limit of 50mg/l (Fig. 5).

5.0	CONCLUSION

The microorganisms show capability for bioremediation of the tanneries waste hence could be effective for the overall management of tannery wastewater in Kano City. However, there is the need for further work to be carried out on a pilot plant using the microorganisms.

REFERENCE

Aemurerhimen, D.O. (2004): Modern Trends and Strategies for Effective Waste Management Issues in Nigeria, Nigerian Society of Chemical Engineers Proceedings, Port Harcourt. 34: 155–166.

American Public Health Association (APHA), Water Environment Federation (WEF) and American Water Works Association (AWWA), (1998): Standard Methods for the Examination of Water and Wastewater, 20th ed. APHA, WEF and AWWA, USA.

Atlas, R.M. and Bartha R. (1992): Hydrocarbon Biodegradation and Oil Spill Bioremediation. In Marshall, K.C. (ed). Advances in Microbial Ecology, vol. 12 Plenum, New York, pp. 287–338.

Buba, M.A., Bello, J.A. and Aderemi, B.O. (2004): Tannery Effluent Treatment – Chromium Recovery. Nigerian Society of Chemical Engineers Proceedings, Port Harcourt. 34: 35–40.

Chadderton, R.A. (1988): An Alternative to Water Pollution Controls. Water Research Bulletin. 24: 183–187.

Chin, K.K., Ng, W.I., Ma, A.N. and Wang, K.K. (1987): Treatability Studies of Palm Oil Refinery Wastewaters. Water Science and Technology. 19: 23–29.

Cuenza, M.A. (2004): A Solution for the Treatment of Wastewater from Small- and Medium-Size Food Processing Companies: The Typical Example of Wastewater from Wineries. Case Study.

FEPA, Federal Environmental Protection Agency (1991): Guidelines and Standards for Environmental Pollution Control in Nigeria, FEPA, Lagos, Nigeria.

HACH Company (1997): Water Analysis Handbook, 3rd edition, HACH Company, Loveland, Colorado, USA.

Harrigan, W.F. and MacCance, M.E. (1966): Laboratory Methods in Microbiology – A Code, Press Lond, New York.

Holding, A.I. and Collee, J.G. (1971): Routine Biochemical Test. In Robbons, D.W. (ed.) Methods in Microbiology, Academic Press, London.

Horner, G. (1993): Bioremediation: A Response to Gross Environmental Abuse. Trends Biotechnol. 11, 317–319.

Hughes, R. and Leffson, K. (1953): The Taxonomic Significance of Fermentative Versus Oxidattion Metabolism of Carbohydrates. Journal of Bacteriology. 66:24–28.

Kamaludeen, S.P.B., Arunkumar, K.R., Avudainayagam, S. and Ramasamy, K. (2003): Bioremediation of Chromium Contaminated Environments, Indian Journal of Experimental Biology, 41, 972– 985.

Leahy, J.G. and Colwell, R.R. (1990): Microbial Degradation of Hydrocarbons in the Environment. Microbiology Review. 54, 305–315.

Leavitt, M.E. and Brown, K.L. (1994): Biostimulation versus Bioaugmentation – Three Case Studies. In Hinchee, R. E., Alleman, B. C., Hoeppel, R. E. and Miller, R. N. (eds.) Hydrocarbon Bioremediation, Lewis, Boca Raton, FL., pp. 72–79.

Lee, C.C. and Lin, S.O. (1999): Handbook of Environmental Engineering Calculations. McGraw Hill, New York.

MAPS (2002): Studies for the design of effluent treatment facilities for Kano Metropolis. A report submitted to the Federal Ministry of Environment, Abuja, Nigeria.

More, S.V., John, S., Rao, B.S., Nair, B.U. and Laxman, B.S., (2002): Chromium Removal and Reduction in COD of Tannery Effluents, Indian Journal of Environmental Health, 44(4), 326–328.

Naidu, A.S. (2000): Indian Leather Industry in 21st Century: Challenges and Opportunities, Yojana. March 13.

Orhon, D., Ates E. and Ubay Çokgör, E. (1999): Characterisation and Modelling of Activated Sludge for Tannery Wastewater. Water and Environmental Research. 7(1): 50–63.

Prince, R.C. (1992): Bioremediation of Oil Spills with Particular Reference to the Spill from the Exxon Valdez. In Fry, J.C., Gadd, G.M., Herbert, R.A., Jones, C.W. and Watson-Craik, I.A. (ed), Microbial Control of Pollution Cambridge University press, Cambridge, UK, pp.  19 – 34.

Pritchard, P.H., Mueller, J.G., Rogers, J.C., Kremer, F.V. and Glaser, J.A. (1992): Oil Spill Bioremediation Experiences, Lessons and Results from the Exxon Valdez Oil Spill in Alaska.  Biodegradation. 3: 315–335.

Ramasami, T., Rao, J.R., Chandrababu, N.K., Parthasarathi, K., Rao, P.G., Saravanan, P, Gayatri, R. and Sreeram, K.J. (1999): Journal of the  Society of Leather Technology. 83: 39–45.

Ramos, J.L. and Timmis, K.N. (1987): Experimental Evolution of Catabolic Pathways of Bacteria. Microbiology Science. 4: 228–237.

Rao, J.R., Gayatri, R., Rajaram, R., Nair, B.U. and Ramasami, T. (1999): Biochimistry and  Biophysics Acta. 1452: 595–602.

Rivela, B., Vidal, G., Bolhardt, C. and Mendez, R. (2002): Towards a Cleaner Production: A Case Study in Chilean Tannery, Waste Management and Research .

Seely, H.W. and van Demark, P.J. (1972): Microbes in Action – A Laboratory Manual of Microbiology. 2nd ed. W.A. Freen and Co., San Francisco.

Tare, V., Gupta, S. and Bose, P. (2003): Case Studies on Biological Treatment of Tannery Effluents in India. Journal of Air & Waste Management Association. 53: 976–982.

Tripathi, R.D. (1978): Effects of Effluents of Chemical and Fertilizer Factory on Germination and mineral Composition of Wheat. Indian Journal of  Ecology. 5:128–133.

Tűnay, O., Kabdasli, I., Orthon, D. and Ates, E. (1995): Characterisation and Pollution Profile of Leather Tanning Industry in Turkey, Water Science and  Technology. 32(12): 1–9.

UNEP/IEO (1994): Tanneries and the Environment: A Technical Guide to Reducing the Environmental Impacts of Tannery Operations, Technical Report No. 4, 120p.

UNIDO (2000): [Buljan, J., Reich, G. and Ludvik J.] Mass Balance in Leather Processing. UNIDO, Vienna. Project No. US/RAS/92/120, 9 August 2000.

World Bank, (1998): Pollution Prevention and Abatement Handbook – Sub-sectorial Environmental Guidelines (Tanneries and Leather Products), Environmental Department, World Bank, Washington, D. C.

Yadav, S., Shukla, O.P. and Rai, U.N. (2005): Chromium Pollution and Bioremediation, EnviroNews, 11 (1).

Yusuf, R.O. (2004): Physico–chemical Properties of Aqueous Effluents of some Industries in Kaduna, Nigeria. LAUTECH Journal of Engineering and Technology. 2(1), 64–72.